## Slide 1: Applying Model Based Design for Quad-Rotor Control System
Presenter: Sang-Ho Yoon
Senior Application Engineer

## Slide 2: Today’s Agenda
Control System Design Challenge
Quad-Rotor Vehicle Modeling
  Multi-domain physical modeling using Simscape
  SimMechanics including CAD file import
Controller Design and Implementation
  Design with Requirement
  Controller Tuning
  Code Generation
Team-Based Development with Simulink Projects
Software Engineering
  Hybrid Simulink-UML Workflow
Questions and Answers
Notes: Review agenda and timing.

## Slide 3: Control System Design Challenge

## Slide 4: Control System Design Challenge
Plant
Controller
s1
s2
s3
System
Actuators
Sensors
Controller
Plant
Controller
Plant
Notes: Key Message is ALL PLANTS HAVE CONTROL SYSTEMS
IF YOU ARE MODELING A PLANT,
YOU NEED TO MODEL CONTROL SYSTEM, TOO

## Slide 5: Control System Design Challenge
Need to simulate plant and controller in one environment to optimize system-level performance.
Controls engineers and domain specialists need to work together to detect integration issues in simulation.
Plant
+
u
y
Controller
s1
s2
s3
System
Actuators
Sensors
Notes: Key Message
Develop_Controller_And_Plant_In_One_Environment
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Develop_Controller_And_Plant_In_One_Environment

## Slide 6: Plant (Quad-Rotor Vehicle) Modeling

## Slide 7: Electrical Systems in Equations
    DC Motor
R
L
Kt,Ke
J,b
θ
i
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations

## Slide 8: Mechanical Systems in Equations
    Simple Pendulum
ΣTz = Iθ1
-mgl*sin(θ1)= ml2θ1
θ1 = - sin(θ1)
..
..
θ
1
x
y
z
mg
l
..
g
l
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations

## Slide 9: Mechanical Systems in Equations
θ
2
m2g
θ
1
x
y
z
m1g
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations

## Slide 10: Mechanical Systems in Equations
θ
2
m2g
θ
1
x
y
z
m1g
θ
3
m3g
m4g
m5g
θ
5
θ
4
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations

## Slide 11: Physical Systems in Simulink
Multibody mechanics (3-D)
Mechanical systems (1-D)
Fluid power and control
Multidomain physical systems
Electrical power systems
Electromechanical and electronic systems
SimMechanics
SimDriveline
SimHydraulics
SimElectronics
SimPowerSystems
Simscape
MATLAB, Simulink
SimMechanics
SimDriveline
SimHydraulics
SimElectronics
SimPowerSystems
Simscape
Mechanical
Hydraulic
Electrical
Thermal Liquid
Custom Domains via Simscape Language
Pneumatic
Magnetic
N
S

## Slide 12: Electrical Systems in Simscape
    DC Motor
Simscape model advantages:
  Easier to read than equations
  Quicker to create
  More intuitive – easier to explain to other engineers
R
L
Kt,Ke
J,b
i
θ
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations

## Slide 13: Modeling 3D Mechanical Systems
Build a model whose structure represents the system:
  Parts (mass, inertia)
  Coordinate systems
  Joints and constraints
Save subsystems for reuse in other models
Parameterize model using MATLAB variables
Connect directly to Simscape and Simulink
Notes: R2012a: Second Generation technology added to SimMechanics

## Slide 14: Import CAD Data Using SimMechanics Link
Automatically create SimMechanics models from a CAD assembly
  Converts mass and inertia to rigid bodies
  Converts mate definitions to joints
  Creates STL files for use with SimMechanics visualization
Directly connects SolidWorks, ProEngineer and Inventor
Public API for other CAD tools
Free download from www.mathworks.com
Notes: R2012b: Import from SolidWorks, ProEngineer, and Inventor supported (model update not supported yet)

## Slide 15: Save Time
Physical Modeling
MATLAB, Simulink
Plant
Model
Domain Knowledge
Programming Effort
Program Effort
Domain Knowledge
Mechanical
Electronic
Multidomain
Hydraulic
Power Systems
Plant
Specification
Fortran, C++
Domain Knowledge
Programming Effort
Notes: Key Message
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Saves_Deriving_and_Programming_Equations
http://www-internal.mathworks.com/wiki/index.php/Physical_Modeling_Tools_Key_Messages#Reduces_Required_Domain_Knowledge
Our Solution The Physical Modeling tools contain extensive libraries of basic building blocks with domain knowledge built in, allowing users to create useful and accurate models even if they do not have extensive experience in the domain.
The Physical Modeling tools enable enable modeling and simulation of physical systems without deriving and programming equations, allowing users without strong mathematic or programming backgrounds to easily create accurate and intuitive models.

## Slide 16: Modeling Quad-Rotor Vehicle
Provided SolidWorks model specifying the vehicle geometry

## Slide 17: Modeling Quad-Rotor Vehicle
Provided SolidWorks model specifying the vehicle geometry
Create dynamic model using SimMechanics Link
Model motors in SimElectronics

## Slide 18: Modeling Quad-Rotor Vehicle
Use basic propeller equations to define forces and moments from props for initial design (Vehicle-ground interaction)
Add external force to represent collision with ground
Verify and improve design with vehicle and MathWorks tools

## Slide 19: Controller Design with Requirement

## Slide 20: Quad-Rotor Control Algorithm Model
Functional Requirements
Simple TCU Model
Notes: So we have created SBR algorithm model from the requirement!
>> sbr ( show the complete SBR algorithm model)
Do simple testing with constant blocks as inputs and display as output or
>>sbr_testHarness_simple

## Slide 21
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Generate
Generate
Hand- Generate
Requirements
Requirements
Create executable specifications
Design with simulation
Advantages:
  Eliminate ambiguity
  Facilitate team communication and component-based modeling
  Analyze and improve requirements and design through simulation
  Test system performance before building physical prototypes
  Automate document generation
Modeling with Simulink

## Slide 22: Traceability
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Functional Requirements
Generate
Generate
Tracing RequirementsModel Simulink® Verification and Validation™
Tracing ModelSource Code Embedded Coder™
Tracing RequirementsSource Code Simulink Verification and Validation
Hand- Generate
Notes: The left side of the diagram represents the design process that goes from high level requirements, and design, elaboration and implementation. All the way to deployment on the target. (click)
Traditionally, the majority of the verification and validation effort happens at the SW and SW/HW integration phase. (click)
What we are going to focus on today are methods for early verification and validation that allow you to shift a portion of your V&V effort earlier in the development and allow you to find and fix problems earlier. These early V&V methods are enabled through the use of MBD and I hope that after this sess

## Slide 23
Creating links between textual documents and model objects
Tracing RequirementsModel Simulink Verification and Validation
Notes: Suggestion for the presenter: Highlight the key features mentioned on the slide and then talk about the benefits of requirements linking – why is this important for the customer.
Typically requirements are scattered around in different documents, whether it is a managed environment, or not. Simulink and Stateflow models are used in conjunction with these predominantly textual documents to describe the details of the design. This situation raises many challenges – models and textual documents can get out of sync, it is difficult to navigate to the right requirement, especially if there are multiple versions of it – whether it is to review the latest revision, or to write a requirement.
To address these problems Simulink Verification and Validation provides an infrastructure that allows you to link a particular document paragraph to any block, state, or transition in the model. Typically this capability is used to assign high level requirements to subsystems, or low level requirements to specific implementation details, or even component tests in Simulink.
The supported format for textual documents are… (list)
The requirements linking capability has several features that can help you review traceability between the model and the text and if RTW-EC is used for code generation, linked textual information can be propagated to the generated code in form of code comments.

## Slide 24: Requirements Traceability – Report Simulink Verification and Validation
Requirements Report provides screenshots of the model and lists all the associated requirements

## Slide 25: Controller Tuning

## Slide 26: Simulink PID Controller Blocks
I, P, PD, PI, PID with approximate derivative
Parallel and ideal forms
Output saturation limits
Integrator anti-windup
Tracking mode for bumpless transfer

## Slide 27: Tuning Challenges
Finding gains values to meet response time and overshoot (phase margin) specifications
  Manual tuning is purely trial and error process, time consuming and non-systematic. It may not produce optimal design and can lead to dangerous conditions
  Rule-based tuning requires a lot of work, or simply cannot be applied (open-loop unstable systems). It cannot be fine tuned
?
?
?

## Slide 28: Solution: PID Tuner
Automatically finds gain values to meet specifications
Provides additional fine-tuning capability with simple sliders
Supports all types of plants
Requires Simulink Control Design
Notes: Mention that tuner linearizes the model at a specific operating point

## Slide 29: Code Generation

## Slide 30: Code Generation
Use of Legacy Code Tool for introduction of existing C code on Simulink models
ISO ANSI-C production code generation with Embedded Coder.
Possible prototyping on target
Run-time errors verification with Polyspace before the compilation phase and execution on the target
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Generate
Generate
Hand- Generate
Requirements
Requirements

## Slide 31: Simple Software Architecture
Core
Software
Algorithms and Logic
Input
Drivers
Output
Drivers
Special
Device
Drivers
Comm
Drivers
Scheduler/Operating System
And Support Utilities
Communication
Interfaces
Sensors
Actuators
Special
Interfaces
ASAP2
CCP
Most Development is on Core Software Algorithms
Notes: A typical ECU with software has an architecture that separates the core algorithm code from the drivers, RTOS and special support software. The drivers support communication interfaces (CAN, LIN, etc), sensors , actuator control and interfacing to special tools (calibration, diagnostics, data acquisition).
The ECU software usually has a scheduler or RTOS that determines how the software should execute and respond to stimuli.

## Slide 32: Interfacing Generated Code
Env. Code
OS/Scheduler
Device Drivers
(CAN,DIO,AIN)
- Diagnosis, etc
EC Code
Model Functions
Parameters, Data
(e.g. Global Var.)
Header Files
(e.g. Extern Var.)
Call Model Functions
(e.g. Model_Step())
Share entry points, data and parameters with header files
Call generated model functions from OS/Scheduler

## Slide 33: Traceability
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Functional Requirements
Generate
Generate
Tracing RequirementsModel Simulink® Verification and Validation™
Tracing ModelSource Code Embedded Coder™
Tracing RequirementsSource Code Simulink Verification and Validation
Hand- Generate
Notes: The left side of the diagram represents the design process that goes from high level requirements, and design, elaboration and implementation. All the way to deployment on the target. (click)
Traditionally, the majority of the verification and validation effort happens at the SW and SW/HW integration phase. (click)
What we are going to focus on today are methods for early verification and validation that allow you to shift a portion of your V&V effort earlier in the development and allow you to find and fix problems earlier. These early V&V methods are enabled through the use of MBD and I hope that after this sess

## Slide 34: Example of HTML Report
Hyperlink back
to model.
Hyperlink within
C code files.
Hyperlink from model to code.

## Slide 35
Including requirements in the generated source code
Tracing RequirementsSource Code Simulink Verification and Validation Embedded Coder
Notes: Suggestion for the presenter: Highlight the key features mentioned on the slide and then talk about the benefits of requirements linking – why is this important for the customer.
Typically requirements are scattered around in different documents, whether it is a managed environment, or not. Simulink and Stateflow models are used in conjunction with these predominantly textual documents to describe the details of the design. This situation raises many challenges – models and textual documents can get out of sync, it is difficult to navigate to the right requirement, especially if there are multiple versions of it – whether it is to review the latest revision, or to write a requirement.
To address these problems Simulink Verification and Validation provides an infrastructure that allows you to link a particular document paragraph to any block, state, or transition in the model. Typically this capability is used to assign high level requirements to subsystems, or low level requirements to specific implementation details, or even component tests in Simulink.
The supported format for textual documents are… (list)
The requirements linking capability has several features that can help you review traceability between the model and the text and if RTW-EC is used for code generation, linked textual information can be propagated to the generated code in form of code comments.

## Slide 36: Simulink Projects

## Slide 37: Model-Based Design workflow
Embedded System
System Model
Mathematical
Model
C & HDL
Plant
Model
Controller
Implementation
Controller
Model
Plant
Hardware
Notes: If you have been to any of our other seminars, you would have seen MathWorks discuss how Model-Based Design can be applied the development of such a controller. Also, a typical Model-Based Design workflow consists of developing the controller leveraging a model of the plant. In this case, our task is to develop the motor controller leveraging design with simulation and generating the controller implementation which could be c-code or HDL.
As previously mentioned, a complex design such as this will require a team of different disciplines. In this case there will be an engineer whose job is to design the motor. Another engineer whose job is to design the controller by working with the motor engineer to understand the characteristics of the motor. An engineer whose job is to implement the controller via C or HDL and work closely with the controls engineer to ensure any implementation constraints don’t negatively impact the original design. Each of these three engineers must be able to efficiently work together often times in parallel.

## Slide 38: Complex designs require multiple disciplines
C & HDL
Notes: These three engineers have the same end goal which is to deliver a spindle motor drive system, but they each focus on a different aspect of the design.
We have a motor engineer (green) who is tasked with the development of the physical motor. A motor engineer typically thinks about the physical characteristics of the motor and typically does motor design simulation using an FEA based tool.
The controls engineer is tasked with the development of the controls of the motor. The controls engineer will be thinking about algorithms which can be used to drive the motor and the system performance. It is common to develop these controls algorithms in Simulink and analyze system performance through simulation.
The software engineer will focus on implementing the controls algorithms on the physical hardware through C-code or potentially HDL. They will be very familiar with the C language and will have concerns of the complexity of the algorithm and the required processor resources to implement these algorithms.

## Slide 39: Considerations for reproducing the project across the design team
Share · Standardize · Iterate
Project file management
Version control
Project initialization and termination

## Slide 40: Organize, Manage
Compare changes
HDL

## Slide 41: Source Control Integration
Local Version Control
Subversion/Git
Other Version Control Tools
Integrate with 3rd party revision
control tools
Basic revision control
  Lightweight local version control tool for single user
  Basic integration with Subversion (SVN) and Git
Adaptor SDK free download available for integration between Simulink Projects and 3rd revision control tools
Developed
with SDK

## Slide 42: Software Engineering

## Slide 43: Modeling Complex Software Systems
Hand Code
UML
Architectural Complexity
Algorithmic Complexity
UML and Simulink
Hybrid
Vendors
IBM Rhapsody
ARTiSAN Studio
IBM Rational System Designer
No Magic Magic Draw
Simulink
Stateflow
Embedded MATLAB
Notes: UML is becoming popular where the architectural complexity of the system is high but does not help designers deal with high algorithmic complexity.
In our market, the UML tools being considered by our customers for such a hybrid solution are (in alphabetical order):
  ARTiSAN Studio
  IBM Rational System Designer
  Kennedy-Carter iUML
  IBM Telelogic Rhapsody
An approach that is beginning to be explored for the design of larger systems with a complex architecture and high algorithmic complexity is to use a hybrid of UML and Simulink
In a hybrid solution UML is often introduced in order to:
  Describe the deployment of software components on a distributed deployment platform
  Define reusable components, often using object-oriented techniques
  Define the services offered by a software platform, such as middleware
  Assemble components from different application domains, for example, graphical user interfaces and control algorithms
Hybrid development poses logistical challenges, not least in the need for expertise in and integration between two different technologies and tool chains. So it may be that where the case for hybrid development can be made but not strongly, a compromise approach using just the Simulink toolset may be the most effective option. It is worth reviewing the features of Simulink that support component-based modeling to determine whether they are sufficient to meet your software development needs.

## Slide 44: Projects with Low Algorithm Complexity and High Architectural Complexity
Example applications:
  User interfaces
  Data management
+ means IDE links the code together
Architectural Complexity
Algorithmic Complexity
Architecture Modeling
UML
Algorithm Code
Non-Algorithmic & Interface Code
+
Drivers
IDE Tool Chain
UML Coder
Parse Algorithm Interface
Use
Cases
Classes
Sequence
Diagrams
Composite
Structure
Diagrams
State
Machines
Notes: Where algorithmic complexity is low (or perhaps the algorithms are pre-existing in code form) Simulink may not be required.
Nonetheless, if there are architectural challenges, a UML tool may be useful.
In this approach, drivers and (existing) algorithmic code are maintained in the Integrated Development Environment (IDE)
The software architecture and interfaces, and must of the non-algorithmic code are designed and maintained in the UML tool.
In order to provide a complete picture of the software architecture, the interface to legacy code can (depending on tool and programming language) be parsed into the UML tool. Code can be generated from the UML tool for those parts of the system for which it is responsible – often this code is mostly just a framework into which code is added in the IDE but sometimes functional behavior is added in the UML design and code generated from that, The most common example of this is the use of UML state charts to describe event-based behavior.

## Slide 45: Projects with High Algorithm Complexity and Low/Moderate Architectural Complexity
Example applications:
  Controllers (avionics, powertrain)
  Signal processing
+ means IDE links the code together
Architectural Complexity
Algorithmic Complexity
Algorithm Modeling
MATLAB
Simulink
Blocksets
Embedded Coder
Legacy Code/ S-Function Import
Stateflow
Algorithm Code
Non-Algorithmic & Interface Code
+
Drivers
IDE Tool Chain
Notes: Where the architectural requirements of a software system are not high, then a Simulink-based software architecture may suffice.
Where Simulink is used it generally maintains the lion’s share of the algorithmic code but there is often legacy algorithmic code that can be integrated into the Simulink design using the legacy code tool, or directly as one or more S-Functions.
In these types of system the non-algorithmic code and interface logic is often fairly straightforward and so can be coded directly in the IDE.

## Slide 46: Projects with High Algorithmic and Architectural Complexity
Example applications:
  Command, Control, Communications, Computers and Intelligence
  Tracking systems
+ means IDE links the code together
Architectural Complexity
Algorithmic Complexity
Architecture Modeling
UML
Use
Cases
Classes
Sequence
Diagrams
Composite
Structure
Diagrams
Algorithm Modeling
MATLAB
Simulink
Blocksets
Legacy Code/ S-Function Import
Stateflow
Algorithm Code
Non-Algorithmic & Interface Code
+
Drivers
IDE Tool Chain
UML Coder
Parse Algorithm Interface
Embedded Coder
Notes: Hybrid development involving combined use of UML tools and Simulink may be required if both algorithmic and architectural complexity are high. In this case, typically the algorithmic code is generated from Simulink and the non-algorithmic and interface code is generated from the UML tool.
Existing legacy algorithmic code may need to be reused in the design of a Simulink algorithm. In this case, that code can be wrapped in an S-Function.
It can help to treat algorithmic code as a component in the overall software architecture captured in the UML tool. In that case the parsing capabilities offered by some UML tools can be used to capturing the interface to algorithmic components. This workflow is explored in more detail later.

## Slide 47: Integration Approaches (Manual)
If Simulink model changes, regenerate Embedded Coder code and tweak handcrafted classes.
Best Practice
  Define fewer and larger Simulink “classes”
  Minimize the frequency of code handover
  Perform verification early and often
Handcraft classes corresponding to C++ header files
Compile and link code files from both sources
Simulink and Stateflow
Embedded Coder
C++ Generator
C++
UML Tool
C++
Code from Embedded Coder with C++ option
C++ code from UML tool
Code Integration Environment
Notes: This slide and the slide following focus on the design flows required to support hybrid UML/Simulink development. The first describes a manual approach to integration, the second an automated approach. (Note that although C++ is suggested as the interchange medium, C can also be used.)
The design flow starts with Simulink; code is generated from a Simulink model using RTW/EC.
An engineer analyses this code and constructs a class that precisely describes the header file generated from RTW/EC. Once this is done, this class becomes part of the architecture of the software system and may be referenced by other classes within the software.
Code is then generated from the UML model. This code represents both non-algorithmic classes and other glue code used to facilitate communication between software components. As long as algorithmic components (those described in Simulink) are accurately represented in the UML model, the code generated from the UML model will call the RTW/EC generated code correctly and any required pre-processor directives (like #includes) will be correctly established. This in turn should minimise integration problems during compile and build in the IDE.
In any approach where two tools are being used together there is bound to be overhead imposed by the more complex design flow. To minimise this overhead it is recommended to keep the number of inter-tool transactions as small as possible. Creating larger components in Simulink, perhaps by composing several models together, and performing as much verification as possible in Simulink, thus reducing unnecessary design iterations, can help significantly.

## Slide 48: Integration Approaches (Automated)
Parse C++ header files into UML classes
If Simulink model changes, regenerate the code and re-parse.
Simulink and Stateflow
Embedded Coder
C++ Generator
C++
UML Tool
C++
Code from Embedded Coder with C++ option
C++ code from UML tool
Compile and link code files from both sources
Parse Code
Code Integration Environment
http://www.mathworks.com/videos/hybrid-software-development-with-simulink-and-uml-tools-68870.html?type=shadow
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 49: Demo for Automated Integration Approaches

## Slide 50
Simulink and Stateflow
Simulink and Stateflow
Create software architecture
Simulink and Stateflow
Real-Time Workshop Embedded Coder
UML Tool
C++
Generate code from Real-Time Workshop Embedded Coder with C++ option
S/W
Requirements
Create ‘placeholder’ model
Parse Code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 51: Setting Up A Hybrid Development Project
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
Inserting a Simulink Component into a Software Architecture.
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 52: Create a Simulink Component by defining the interfaces – 1 Input and 2 Output
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 53
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 54: Generate C++ from Simulink component
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 55
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 56
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Parse Code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 57
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Parse Code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 58
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Parse Code
Create software architecture
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 59
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Parse Code
Create software architecture
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 60
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
S/W
Requirements
Develop and test component in Simulink
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 61
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
S/W
Requirements
Generate code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 62
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Re - Parse Code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 63
Simulink and Stateflow
Simulink and Stateflow
Simulink and Stateflow
Embedded Coder
UML Tool
S/W
Requirements
Create ‘placeholder’ model
C++
Re - Parse Code
Notes: Many UML tools do have useful C++ parsing technologies that can be used to read in the code generated from Simulink.
These parsers enable an automated approach where the header files generated from RTW/EC can be automatically imported as classes in the UML model, and when the header files change these classes can be automatically updated. This reduces the incidence of errors due to mistakes in rendering UML classes from header files by hand.
Although this doesn’t tend to work as well for C we do have several customers using an automated C based approach.

## Slide 64: System Engineering

## Slide 65: From Requirements to Architecture and Specification
Architecture
Behavior
Abstract Detailed
Requirements

## Slide 66: What is modeled?
System
Architecture
Software Architecture
System
Behavior
Software
Behavior
Abstract Detailed
Software System

## Slide 67: How it is modeled using SysML/UML
System
Architecture
Software Architecture
System
Behavior
Software
Behavior
Abstract Detailed
Software System
UML
SysML
Tools
  Rhapsody (IBM)
  Magic Draw (No Magic)
  Enterprise Architect (Sparx)
  CORE (ViTech)

## Slide 68: Hybrid Simulink-SysML/UML Workflow
System
Architecture
Software Architecture
System
Behavior
Software
Behavior
Abstract Detailed
Software System
SysML
Simulink
Simulink
UML

## Slide 69: Hybrid Simulink- UML Workflow
Software Architecture
Software
Behavior
Abstract Detailed
Software
Simulink
UML
http://www.mathworks.com/videos/hybrid-software-development-with-simulink-and-uml-tools-68870.html?type=shadow

## Slide 70: Hybrid Simulink-SysML/UML Workflow
System
Architecture
System
Behavior
Abstract Detailed
System
SysML
Simulink

## Slide 71: Hybrid Simulink-SysML/UML Workflow #1
System
Architecture
System
Behavior
Abstract Detailed
SysML
Simulink
Import Architecture

## Slide 72: Hybrid Simulink-SysML/UML Workflow #2
System
Architecture
System
Behavior
Abstract Detailed
SysML
Simulink
Bi-Directional Trace via RMI (in Simulink V&V)

## Slide 73: Hybrid Simulink-SysML/UML Workflow #3
System
Architecture
System
Behavior
Abstract Detailed
SysML
Simulink
Consistency Check

## Slide 74: Hybrid Simulink-SysML/UML Workflows
System
Architecture
System
Behavior
Abstract Detailed
SysML
Simulink
Import Architecture
Consistency Check
Bi-Directional Trace via RMI (in Simulink V&V)

## Slide 75: Questions?
Notes: [Timing: 15 minutes for Intro]