## Slide 1: Model Based Design Workshop
Mark Walker
Sylvain Sauvage

## Slide 2: Agenda
Overview of Simulink for DO-178
User examples
Workshop structure introduction
  Simulink Projects
  DO-178 Qualification Kit
Software Development Process
Verification of Requirements Process
Verification of Design Process
Verification of Coding and Integration Process
Testing of Integration Process
Verification of Verification Process Results

## Slide 3: Overview of MathWorks Tool Chain R2012b Example of DO-178 Software life-cycle
Trace
Requirements
Models
Verify
C code
EOC
Abbreviations
DV: Simulink Design Verifier
MA: Model Advisor
MC: Model Coverage
RMI: Requirements Management Interface
RTE: Run-Time Error
PIL: Processor-in-the-Loop
SDD: System Design Description
VV: Verification and Validation
Validate
Develop
Compile & Build
Code coverage
DO Qualification Kit
Simulink®
Stateflow®
Simulink® Design VerifierTM
Simulink® Validation VerificationTM (MC)
Simulink® Validation
VerificationTM (MA)
Simulink® Validation
VerificationTM (RMI)
Simulink®
Stateflow®
Simulink® Design VerifierTM
Simulink® CoderTM
xPC TargetTM
Simulink® Code InspectorTM
Polyspace® (MISRA, RTE)
Simulink® Code InspectorTM
Embedded CoderTM (PIL)
SystemTestTM
Polyspace® ( RTE)
Embedded CoderTM (PIL)
SystemTestTM
Polyspace® ( RTE)
Embedded CoderTM
Simulink® Report GeneratorTM (SDD)

## Slide 4: Septentrio
http://www.mathworks.com/tagteam/72275_92004v00_developing-high-integrity-aircraft-approach-systems.pdf

## Slide 5: Eurocopter – EASA – New in 2012

## Slide 6
BAE Utilizes Simulink HDL Coder for DO-254 Level A Project – New in 2012
Challenge
Develop and deploy a control law to an FPGA that can be certified to DO-254 Level A for a commercial business jet.
Solution
Develop control laws in Simulink, link requirements to blocks using Simulink Verification and Validation, and generate HDL code using Simulink HDL Coder.
Results
  Simulink models are used to develop and verify designs, and generate HDL code.
  Generated code is platform independent, readable, and efficient.
  Traceability established between requirements, detailed design expressed in Simulink, and HDL implemented for DO-254 Level A certification.
“Simulink HDL Coder generates readable code that is traceable to the requirements and is critical to our DO-254 Level A certification plans.”
Mike Weaver
Senior Systems Engineer

## Slide 7: Design Times at Honeywell Cut by 60%
Challenge
Update a flight control system while reducing development time and costs
Solution
Use design tools from MathWorks to enable one team to design, model, and simulate the flight-control laws and automatically generate flight-ready code
Results
  A five-to-one improvement in productivity
  Highly accurate, reusable code
  A superior product
“[Using Simulink and Simulink Coder] we found we could do in half a day what previously took a week or more… It is pretty easy to see at least five-to-one improvement over the way we used to work.”
Wayne King
Honeywell Commercial Aviation Systems

## Slide 8
Fairchild Controls Uses Real-Time Workshop Embedded Coder to Generate Flight Code Certified to DO-178B
Challenge
Develop Global Tanker Motor Drive Unit for Boeing 767 in a way that improves quality but reduces costs
Solution
Use Simulink to design the software and detect errors very early in process, then generate flight code automatically
Results
  DO-178B certification achieved
  Generated code ran fast, well within required cycle time
  Device driver code from Target Support Package used in the DO-178B certified application software
  Shorter development time
  More maintainable product
“Automatic code generation is entrenched in our in DO-178B processes. We are excited by the new DO Qualification Kits and MathWorks DO-178C efforts.”
Dr. Haik Biglari, P.E. Senior Director of Engineering Fairchild Controls
40 kW motor drive unit developed using Simulink (read about it here)

## Slide 9: Development of airborne systems Model-Based Design & Certifications
MBD recognized as an efficient approach for developing safety-critical applications
MBD objectives and activities are now better defined (Full definition in DO-178C / DO-331, but you can download this for free)
EASA identifies MATLAB/Simulink as an MBD tool for DO-178B

## Slide 10: Models as High and Low Level Requirements?
DO-178C approach explained by Pierre Lionne at MathWorks Model-Based Design conference for High-Integrity systems (Nov 2011)

## Slide 11: Verification Process
High Level
Requirements
Low Level
Requirements
Executable Object Code
Test (classical)
Notes: Main idea is to verify the EOC by performing tests against 2 diferent levels of abstraction of requirements.

## Slide 12: Verification Process
Test (example #1)
Low Level
Requirements
Executable Object Code
Model = HLR

## Slide 13: Verification Process
High Level
Requirements
Executable Object Code
Test (example #2)
Model = LLR

## Slide 14: Verification Process
Executable Object Code
Test (example #3)
Model = HLR + LLR
?
Notes: In this case we only have one level of abstraction requirements not any more possible…

## Slide 15: Verification Process
Model Parent
Requirements
Executable Object Code
Test (example 3)
Model = HLR + LLR
Notes: This approach is applicable where ever the model and the Model Parent requirements are (system area or SW area)
Remark: Model Parent Requirements is not the terms used in the supplement but this one is more concise and I believe very wel understandable.

## Slide 16: Verification Process
Test (example 3)
When model express both LLR and HLR, it is required to show:
  Compliance & Robustness of EOC with Model
  Compliance & Robustness of EOC with Model Parent Requirements (whatever the process that produced it)

## Slide 17: Simulink Projects

## Slide 18: DO Qualification Kit

## Slide 19: What does the Qualification Kit do?
Help qualify the following tools:
  Simulink Verification and Validation
  Simulink Report Generator
  Simulink Code Inspector
  System Test
  Polyspace
By providing
  Operation requirements for the tools above.
  Test plan and test suite to demonstrate the tool compliance.
  Reference execution of all tests
TOR: Tool Operational Requirements
Details requirement for a tool
TQP: Tool Qualification Plan
How to execute the tests.
Qualkitdo<tool>RunTests.xlsx
Tests/modelnnn.slx
Outputs/modelnnn/
Reports
Generated code
Qualkitdo<tool>RunTests.m
Qualkitdo<tool>RunTests.rpt
TCPR: Test Cases, Procedures and Results
Verify
Plan
Tests/modelnnn.slx
Tests/modelnnn.slx
Tests/modelnnn.slx
Compare and Report
Qualification Kit Workflow
Workflow for Using MBD and The MathWorks tools
Defines the usage of tools for each DO178 objective.
DO178
Qualify tools
For each tool

## Slide 20: DO-178C Structure TBD
DO-178C 1.0
Introduction
DO-178C 2.0
System Aspects relating to Software Development
Software Life Cycle
DO-178C 4.0
DO-178C 5.0
DO-178C 6.0
DO-178C 7.0
Software Planning Process
Software Development Process
Software Verification Process
Software Configuration Management Process
DO-178C 8.0
DO-178C 9.0
DO-178C 10.0
Software Quality Assurance Process
Certification Liaison Process
Overview of Certification Process
DO-178C 3.0
DO-178C 11.0
Software Life Cycle Data
DO-178C 12.0
Additional Considerations
Model-Based Design
Early verification and validation
Code generation
Tool classification and qualification
Notes: DO-178C dash 6 is concerned with software development processes and includes information on the usage of MBD, early V&V (such as testing at the model level) and PCG
Part 8 is covers among other supporting processes tool qualification topics

## Slide 21: TBC DO-178C Reference Workflow Verification and Validation of Models and Generated Code
Model Verification
Code Verification
Discover design errors at design time
Gain confidence in the generated code
Notes: - Tool Chain example (not all steps/tools are mandatory)
- Integrated tool chain, covering both Software development as well as verification and validation)

## Slide 22: DO-178C Reference Workflow Example Tool Chain
PIL testing / CGV (Embedded Coder), Test generation (SLDV)
Traceability report (Embedded Coder), Traceability matrix generation (IEC Cert Kit),
Bullseye code coverage integration (Embedded Coder)
Simulink, Model coverage (SLVnV),
Requirements Management Interface (SLVnV)
Model Advisor (SLVnV),
Property proving (SLDV)
Simulink, Stateflow, Simulink Fixed Point
Embedded Coder
MathWorks provides an integrated tool chain for DO-178C
TBD
Notes: - Tool Chain example (not all steps/tools are mandatory)
- Integrated tool chain, covering both Software development as well as verification and validation)

## Slide 23: Software Development Process (1)
Defined by “derived requirement” link.
Model used for high level requirements or parent requirements linked to model
Model Reference hierarchy defines software architecture

## Slide 24: Model Development

## Slide 25: Requirements Linking

## Slide 26: Software Development Process (2)
S1: System Design Description Report
Developed as a Simulink model
S6: Generate Code

## Slide 27: System Design Description Report

## Slide 28: Web View

## Slide 29: Generated Code

## Slide 30: Software Development Process (3)
Compilation triggered from Embedded Coder build
S9: Traceability report
S8: Simulink Code Inspector traceability report
As above
As above

## Slide 31: Verification of Requirements Process (1)
S1: System design description
S4: Model tests (includes coverage)
As above
As above
As above (SLDV also helps identify unreachable requirements)

## Slide 32: Coverage Reports
2
1

## Slide 33: Verification of Requirements Process (2)
S5: Model tests
S9: Traceability report
S3: Model advisor checks
As above
As above
As above
S9: Traceability report

## Slide 34: Model Advisor Checks

## Slide 35: Verification of Design Process (1)
S1: SDD
S3: Model Advisor
S1: SDD
S4: Model review
Model analysis
S5: Simulation
S1: Report
S3: Model Advisor
S5 Model tests
S3: Model Advisor
S5: Use per-component test cases

## Slide 36: Execute Model Simulation

## Slide 37: Verification of Design Process (2)
S5, S7:Review test execution reports
S9: Review traceability reports
S1: Generate SDD,
Dependency viewer
S1: Generate SDD,
S3: Advisor
S1: Generate SDD
S7: Run equivalence tests
S3, DO-178 and MAB checks

## Slide 38: Verification of Design Process (3)
Review test cases
S5, S7:Review test execution reports
S5, S7:Review test execution reports

## Slide 39: Traceability Report
Tools and Formats:
  Word, Excel, DOORS, MuPAD
  text, html, pdf, URL

## Slide 40: Verification of Coding and Integration Process (1)
As above
S8: Code inspector
S8 Code Inspector.
Polyspace (not shown in workshop)
S8: Code inspector,
Polyspace

## Slide 41: Measure Equivalence vs. Implementation
Independently verify that Embedded Coder generated code traces to and complies with low-level requirements
Demonstrate that model and source code match structurally and functionally
Provide model code traceability data
Eliminate/reduce manual code reviews for DO-178 software
Same certification credits as qualified code generator
Embedded Coder
Code
verification
Code traceability
Source code
Model
Notes: Must be suitable for customers as the slide will be made available for external use at the time of release.
Motivation
One or two sentences describing the problem in terms of how customers phrased or think of the issue. Consider both the feature and the workflow motivations.
Solution (Added Details)
More details as appropriate. How does it integrate with other features and products?
Doc Reference
In addition to release notes, which should be the source for most of the information on this slide. Add a doc reference if possible.
Demo
Shipping demo name
Limitations, Known Problems, and Workarounds
What are the current limitations? Are there problems end users are likely to run into? Are there Workarounds? Is anything likely to break, not just feature or product but interoperability with other products?
Questions and Debugging Tips (for MathWorks Support team)
What questions might end users ask?
What should Support try out when end users run into problems?
Are there any debugging tips or processes Support should follow?
Release Number – Tech Marketing to add icon closer to release date.

## Slide 42: Simulink Code Inspector

## Slide 43: Simulink Code Inspector
Will accept:
  Renaming, Reordering of local variables
  Swapping independent lines of code
  Swapping ‘+’ or ‘*’ operands
  New or deleted comments
Will accept and warn:
  Introducing extra local variables and splitting a line of code using them
  Transform ‘3.0’ to ‘(2.0+1.0)’
  Adding harmless lines ‘u=u+0.0;’
Will not validate
  True changes
    Deleted code
    Added code
    Constant values
    Operators
    Incorrect type cast
    Operands
    Out of order execution
    Syntax errors (e.g. remove ‘{’ or ‘;’)
  Negating a condition and swapping if and else clauses
  Changes in local variables’ scope
  Replace ‘if(a)’ by ‘if(a!=0)’

## Slide 44: Verification of Coding and Integrating Process (2)
Polyspace (not shown in workshop)
S8: Code Inspector, Polyspace
As above
As above
As above

## Slide 45: EOC Equivalence Tests

## Slide 46: Testing of Integration Process (1)
As above
S7: As per S7 but PIL not SIL mode
As above

## Slide 47: Testing of Integration Process (2)
As above
As above

## Slide 48: Verification of Verification Process Results (1)
S5 and S7 reports
S5 and S7 reports
As above
Not included

## Slide 49: Verification of Verification Process Results (2)

## Slide 50: Verification of Verification Process Results (3)
As above
Not shown in workshop
As above

## Slide 51: Verification of Verification Process Results (4)
As above
As above

## Slide 52: Software Configuration Management Process
S9: Traceability reports
CM Integration
Dependency analysis
Tools:
  Currently supported: Subversion, In development: GIT
  Commercial tools being developed by respective vendors.

## Slide 53: Overview of MathWorks Tool Chain R2012b Example of DO-178 Software life-cycle
Trace
Requirements
Models
Verify
C code
EOC
Abbreviations
DV: Simulink Design Verifier
MA: Model Advisor
MC: Model Coverage
RMI: Requirements Management Interface
RTE: Run-Time Error
PIL: Processor-in-the-Loop
SDD: System Design Description
VV: Verification and Validation
Validate
Develop
Compile & Build
Code coverage
DO Qualification Kit
Simulink®
Stateflow®
Simulink® Design VerifierTM
Simulink® Validation VerificationTM (MC)
Simulink® Validation
VerificationTM (MA)
Simulink® Validation
VerificationTM (RMI)
Simulink®
Stateflow®
Simulink® Design VerifierTM
Simulink® CoderTM
xPC TargetTM
Simulink® Code InspectorTM
Polyspace® (MISRA, RTE)
Simulink® Code InspectorTM
Embedded CoderTM (PIL)
SystemTestTM
Polyspace® ( RTE)
Embedded CoderTM (PIL)
SystemTestTM
Polyspace® ( RTE)
Embedded CoderTM
Simulink® Report GeneratorTM (SDD)

## Slide 54: Process Deployment Advisory Services Quickly Adopt Model-Based Design for DO-178
Provides key ingredients necessary to accelerate transition towards DO-178 compatible processes and tool chains for Model-Based Design
Typical deployment service
  Familiarization with existing processes and tools
  Gap analysis
  Targeted instruction
  Hands-on deployment support
http://www.mathworks.com/services/consulting/areas/do-process-deployment.html

## Slide 55: Close
Thank you!
Further information:
  Phil Maltby – Account Manager (phil.maltby@mathworks.com)