## Slide 1: Verification and Validation in Model Based Design
Presenter: Sang-Ho Yoon
Senior Application Engineer

## Slide 2: Today’s Agenda
Introduction to V&V in Model-Based Design
Verification Activities in MBD
Model Verification
  Design Review
  Static Analysis
  Dynamic Test
Code Generation and Verification
  Code Review
  Static Analysis
  Equivalence Test
Questions and Answers
Notes: Review agenda and timing.

## Slide 3: Introduction to V&V in Model-Based Design
윤 상 호
Senior Application Engineer

## Slide 4
Ind. Standards
Requirements
System-Level
Specification
Subsystem
Design
Subsystem
Implementation
Subsystem
Integration & Test
System-Level
Integration & Test
Complete
Integration
& Test
C, C++
MCU
DSP
FPGA
ASIC
HDL
Generate
Code Verification and Validation
Integration testing
User Acceptance Testing
Requirements
Physical
Components
Environment
Algorithms
Verification and Validation
Development Process
Notes: So to explain model based design we first need to look at the problems typically associated with a traditional development process.
We will use a design V, common in Automotive and familiar in some Aerospace companies and other industries.
The “V” is a 2D view of a development process – the x-axiz is time, while the y-axiz is abstraction. As you move down the left hand side of the V you add more and more details to the design with implementation at the vertex. As you move up the right hand side of the V, you do higher and higher levels of integration and test with final working products at the end.
[Build, step through animation]
We can generalize this process into the phases of specification, designing, implementing, and testing,
Additional notes
Projects start with a definition of the requirements of the product to be created.
This set of requirements leads to a specification of the system. Then each subsystem is designed and implemented. How this is done depends a lot on the product involved and its complexity. We won’t try to capture all possible ways that this can be accomplished. But as you move further down, you add additional detail. With implementation at the Apex.
With all subsystems designed and implemented, integration and test begins, at higher and higher levels, leading ultimately to a final, working product.

## Slide 5: Price of Late Verification and Validation Relative Cost to Fix Defects
Source: Return on Investment for Independent Verification & Validation, NASA, 2004.
High cost of fixing defects detected late
Difficult to know when “enough” testing is done
As design complexity increases, time and cost to test does too
Requirements
Design
Code
Test
Test
Code
Design
Requirements
0
5
10
15
20
25
30
35
40
45
50
Relative Cost
to Fix
Phase Found
Defect
Type
Relative Cost to Fix Defects per Phase Found
Test
Code
Design
Requirements

## Slide 6: Reference Workflow for Verification and Validation in Model-Based Design
Model Verification
Code Verification

## Slide 7: Verification Activities in MBD

## Slide 8: Verification in DO-178B/C
*DO-178C Section 6.0

## Slide 9: Verification Activities in MBD
Model Verification
  Design Review
    Requirement Traceability
    Report Generation
  Static Analysis
    Model Standards Checking
    Design Error Detection
    Prove Design Correctness
  Dynamic Test
    Simulation-based Functional Test
    Coverage Analysis
Code Generation and Verification
  Code Review
    Code Inspection
  Static Analysis
    Code Metrics and Coding Rule Checking
    Formal Verification (Abstract Interpretation)
  Equivalence Test
    SIL(Software-In-the-Loop) and PIL(Processor)
Requirements
Model
Design
Code
Integration
User Acceptance
1
2
Code

## Slide 10: Model Verification

## Slide 11: 1) Design Review

## Slide 12: Algorithm Model
Functional Requirements
Model
Notes: So we have created SBR algorithm model from the requirement!
>> sbr ( show the complete SBR algorithm model)
Do simple testing with constant blocks as inputs and display as output or
>>sbr_testHarness_simple

## Slide 13: Traceability
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Functional Requirements
Generate
Generate
Tracing RequirementsModel Simulink® Verification and Validation™
Tracing ModelSource Code Embedded Coder™
Tracing RequirementsSource Code Simulink Verification and Validation
Hand- Generate
Notes: The left side of the diagram represents the design process that goes from high level requirements, and design, elaboration and implementation. All the way to deployment on the target. (click)
Traditionally, the majority of the verification and validation effort happens at the SW and SW/HW integration phase. (click)
What we are going to focus on today are methods for early verification and validation that allow you to shift a portion of your V&V effort earlier in the development and allow you to find and fix problems earlier. These early V&V methods are enabled through the use of MBD and I hope that after this sess

## Slide 14
Creating links between textual documents and model objects
Tracing RequirementsModel Simulink Verification and Validation
Notes: Suggestion for the presenter: Highlight the key features mentioned on the slide and then talk about the benefits of requirements linking – why is this important for the customer.
Typically requirements are scattered around in different documents, whether it is a managed environment, or not. Simulink and Stateflow models are used in conjunction with these predominantly textual documents to describe the details of the design. This situation raises many challenges – models and textual documents can get out of sync, it is difficult to navigate to the right requirement, especially if there are multiple versions of it – whether it is to review the latest revision, or to write a requirement.
To address these problems Simulink Verification and Validation provides an infrastructure that allows you to link a particular document paragraph to any block, state, or transition in the model. Typically this capability is used to assign high level requirements to subsystems, or low level requirements to specific implementation details, or even component tests in Simulink.
The supported format for textual documents are… (list)
The requirements linking capability has several features that can help you review traceability between the model and the text and if RTW-EC is used for code generation, linked textual information can be propagated to the generated code in form of code comments.

## Slide 15: Requirements Traceability – Report Simulink Verification and Validation
Requirements Report provides screenshots of the model and lists all the associated requirements

## Slide 16: Report for Model Review Simulink Report Generator
Design and generate reports for MBD
Interactive design reviews
Model Comparison and Merge

## Slide 17: 2) Static Analysis

## Slide 18: Modeling Standards Checking Overview Simulink Verification and Validation
Static analysis of models against a set of checks
  Checks for simulation
  Checks for code generation
  Requirements Consistency
  Modeling Standards
Modeling Standards Checks for:
  MAAB Style Guidelines
  DO-178B
  IEC 61508
  ISO 26262
Extensibility API

## Slide 19: Modeling Guidelines for High-Integrity Systems
Leverage industry-best practices and MathWorks tool expertise when developing high-integrity systems
Modeling Guidelines and corresponding Model Advisor checks to facilitate modeling standards and guidelines objectives of ISO 26262, IEC 61508, DO-178B/C, and MISRA-C
http://www.mathworks.com/help/pdf_doc/simulink/hi_guidelines.pdf

## Slide 20: Identifying Design Errors Early Simulink Design Verifier
Automatic identification of hard-to-find design inconsistencies in the model without running simulation
Integer overflow
Division by zero
Dead logic
Assertion violation
Notes: This is new functionality in R2011a. Unlike with test generation, where simulation is used to run a number of tests and where outputs of the model need to be monitored and data analyzed in order to discover faulty behavior, as of R2011a a number of potential design problems can be detected automatically, before running simulation and before testing.

## Slide 21: Verifying Design Against Requirements Simulink Design Verifier
Must do
Must never do
Model Requirements
Prove Design Correctness

## Slide 22: Simulink Test Tool for authoring, managing, and executing simulation-based tests
Test Harnesses
  Synchronized testing environment
  Enables unit testing without requiring new model
  Component or system
  Configure, build, simulate
  Supports SIL, or PIL
  Supports direct “adhoc” testing
Main Model
Test Harness
synchronized
Component under test
Exercise
Analyze

## Slide 23: 3) Dynamic Test

## Slide 24
Test Cases
Signal Builder
Test Cases to Signal Builder
Notes: Now is the time to revisit Testing Requirements. Revise the test cases in sbr_testing_requirements.doc.
First show how the first test case can be easily created using Signal Builder
  Key : Constant at 0
  SeatBeltFasten : Square wave at frequency 2
  Speed : Triangle wave at default setting
  SeatBeltIconExp : Constant at 0
Now, Let’s make use of the sbrTestCase.xls file.
  Open xlsSignalGui
  Push open button and select sbrTestCase.xls file
  Press generate button
  A Signal Builder block will be created into a Simulink model
  # There is a bug on using commands to create Signal Builder block. After the block gets generated click all the test case tabs to overcome this issue!

## Slide 25
Test-Harness
Test Cases (Signal Builder)
Output Check (Assertion Block)
Model
(Model Block)
Module Test-Harness
Notes: Three aspects of test-harness
Test Cases (Signal Budiler)
Model under test (Model Block can be used to bring sbr.mdl into the test-harness environment)
Output check (combination of relational operators and assertion block is being used)
>> sbr_testHarness
Open the Signal Builder block and explain about the assertion control
Test each test cases one by one
Error will be asserted on TC-04
Turn off the assertion and see the scope to check the difference between simulation result and expected result.
Open Model block parmeters and change sbr -> sbr_fix
Test TC-04 again and finish TC-05
Now the SBR model’s functional testing is done
It is time to talke about test automation and report generation

## Slide 26: Model Coverage Report Simulink Verification and Validation
Coverage metrics identifies untested portions of your model

## Slide 27: Relational Boundary Coverage (R2014b)
Verify testing around boundary points (Part of DO-178C)
Integer Relation
Floating-point Relation
Lhs just < Rhs
Lhs just > Rhs
Lhs just < Rhs
Lhs just > Rhs
Lhs just < Rhs
Lhs just > Rhs
Lhs == Rhs

## Slide 28: Improving Test Suite Simulink Design Verifier
Generating tests to reach coverage criteria
Test generation harness with the copy of the original model
Test inputs that ensure complete
coverage
Test Generation
Notes: >> sbr_testGen
1) Generate test cases using DV.

## Slide 29: Simulink Test Tool for authoring, managing, and executing simulation-based tests
Test Manager
  Create Test Cases
  Group into Suites and Test Files
  Execute individual or batch
  View summary and detailed results
  Archive, export, report

## Slide 30: Test Case Templates
Input
1. Simulation Test
2. Baseline Test
3. Equivalence Test
Expected
Outputs
File
Assessment Criteria
Input
Input
Input
Output
Output
Output
Output
Assessment Criteria
Assessment Criteria

## Slide 31: How about Legacy Code?
Use of Legacy Code Tool for introduction of existing C code on Simulink models
specification
External C Function
MATLAB code

## Slide 32: Coverage for C-code S-Functions
C code
Coverage
Model
Design
S-Function
Notes: In coming releases we plan to extend coverage support to span both code and model aspects.
As a first step, in R2015a we expect to release model coverage extensions for C coded S-Functions. When your model contains instances of C coded S-Functions and you collect model coverage, the generated report will include coverage information for each instance of an S-Function with links to detailed code coverage for the aspects that are active during the model simulation.

## Slide 33: Code Generation and Verification

## Slide 34: Code Generation
ISO ANSI-C production code generation with Embedded Coder.
Use of Legacy Code Tool to make a call to existing C code in generated code from Simulink models
HTML Report Generation for Review and Traceability
FPGA
ASIC
Digital Electronics
VHDL, Verilog
Implement
Integration
DSP
Embedded Software
C, C++
MCU
Design
Physical Components
Environment
Algorithms
Generate
Generate
Hand- Generate
Requirements

## Slide 35: 1) Code Review

## Slide 36: HTML Report
Hyperlink back
to model.
Hyperlink within
C code files.
Hyperlink from model to code.

## Slide 37: Simulink Code Inspector Automate DO-178B Code Reviews
Independently verify that Embedded Coder generated code traces to and complies with low-level requirements
Demonstrate that model and source code match structurally and functionally
Provide modelcode traceability data
Eliminate / reduce manual code reviews for DO-178B software
Same certification credits as qualified code generator
Embedded Coder
Code
verification
Code traceability
Source code
Model
Notes: Must be suitable for customers as the slide will be made available for external use at the time of release.
Motivation
One or two sentences describing the problem in terms of how customers phrased or think of the issue. Consider both the feature and the workflow motivations.
Solution (Added Details)
More details as appropriate. How does it integrate with other features and products?
Doc Reference
In addition to release notes, which should be the source for most of the information on this slide. Add a doc reference if possible.
Demo
Shipping demo name
Limitations, Known Problems, and Workarounds
What are the current limitations? Are there problems end users are likely to run into? Are there Workarounds? Is anything likely to break, not just feature or product but interoperability with other products?
Questions and Debugging Tips (for MathWorks Support team)
What questions might end users ask?
What should Support try out when end users run into problems?
Are there any debugging tips or processes Support should follow?
Release Number – Tech Marketing to add icon closer to release date.

## Slide 38: Simulink Code Inspector Overview
Independent code inspection
Code inspection report

?

Model and code development
Normalized Model IR
Normalized Code IR
Model IR
Code IR
IR transformations
Matching
Embedded Coder
C source code
Simulink Model
Static verification tool, that checks the generated code against model
Automates DO-178B Table A-5 verification activities
Traceability report

## Slide 39: Meeting DO-178 Objectives Anticipated Certification Credits for Simulink Code Inspector with other code verification products
Embedded Coder
Code verification: Simulink Code Inspector
Code traceability: Simulink Code Inspector
Source code
Model
Code conformance: Polyspace
Annex A Table | Objective | DO-178B Ref. | Software Levels | Anticipated Certification Credit [Tool(s)]
A-5 | (1) Source Code complies with low-level requirements | Section 6.3.4a | A, B, C | Full [Simulink Code Inspector]
A-5 | (2) Source Code complies with software architecture | Section 6.3.4b | A, B, C | Full [Simulink Code Inspector]
A-5 | (3) Source Code is verifiable | Section 6.3.4c | A, B | Full [Simulink Code Inspector, Polyspace dead code analysis]
A-5 | (4) Source Code conforms to standards | Section 6.3.4d | A, B, C | Full [Polyspace MISRA-AC ACG rules checker]
A-5 | (5) Source Code is traceable to low-level requirements | Section 6.3.4e | A, B, C | Full [Simulink Code Inspector]
A-5 | (6) Source Code is accurate and consistent | Section 6.3.4f | A, B, C | Full (for source code based criteria) [Simulink Code Inspector, Polyspace verifier]

## Slide 40: 2) Static Analysis

## Slide 41: Runtime Errors
Arithmetic errors
  Found in (code)
    Overflows, division by zero, bit-shifts, square root of negative numbers
  Caused by (model)
    Faulty scaling, changes in or unknown calibrations, untested data ranges coming out of a subsystem into an arithmetic block
Memory corruption
  Found in (code)
    Out of bound array indexes
    Pointer arithmetic
  Caused by (model)
    Array manipulation in Stafeflow
    Hand-written look-up table functions
Data truncation
  Found in (code)
    Overflows
    Wrap around
  Caused by (model)
    Saturations leading to unexpected data flow inside the generated code
Coding errors
  Found in (code)
    Non initialized data
    Dead code leading to unreachable transitions or states
  Caused by (model)
    Faulty Stateflow programming

## Slide 42: CATEGORY OF STATIC ANALYSIS OF USING TOOLS
Compiler Warnings
Bug Findings
Formal Methods
Code Metrics, and Coding Rules
(No False negative)
(False negative)
Error Prevention
Error Detection

## Slide 43: Polyspace PRODUCTS
Compiler Warnings
Bug Findings
Formal Methods
Code Metrics, and Coding Rules
(No False negative)
(False negative)
Polyspace Bug Finder
Polyspace Code Prover
Polyspace Bug Finder
Polyspace Code Prover
Error Prevention
Error Detection

## Slide 44: Polyspace Formal Methods based Static Code Analysis
Exhaustively verify code
  Detect and prove absence of runtime errors
  Precisely determines and propagates variable ranges
Languages supported
  C, C++, and Ada
Verify SW robustness
  Analyze for full range operating conditions
  OR
  Specified ranges of parameters and inputs

## Slide 45: Tracing results back to the model PolySpace™ Model Link SL
Integrates code verification with the production code generation

## Slide 46: 3) Equivalence Test

## Slide 47: Software-in-the-Loop (SIL) Testing: Verify Production Controller with Software-in-the-loop
Compiled C Code
S-Function
(Windows DLL)
Code
Generation
Execution
  Host/Host
  Nonreal-time
Notes:   >> sbr_testHarness_SiL

## Slide 48: Processor-in-the-Loop Testing: Verify Production Controller with Processor-in-the-loop
Production Processor
Code
Generation
Execution
  Host/Target
  Nonreal-time
Notes:   Embedded IDE Link for TS has been used(C167)
  >> sbr_testHarness_PiL

## Slide 49: Standards Compliance
Notes: [Timing: 15 minutes for Intro]

## Slide 50: Traditional DO-178B/C Workflow
Validate
Trace
Code Review
Conformance
Code Review
Trace
Design Review
Conformance
Design Review
Verify
Design Review
Verify
Test Cases & Review
Test Procedures & Review
Test Execution & Review
Code Coverage Tool
Verify
Code Review
Verify
Test Cases & Review
Test Procedures & Review
Test Execution & Review
Code Coverage Tool
Requirements
Design
Source Code
Object Code
Text or
Graphics Editor
Code
IDE

## Slide 51: Workflow Example with MBD
Validate
Embedded Coder
Trace
Embedded Coder
Simulink Code Inspector*
Trace
SLVNV: RMI
SLRG: SDD *
* DO-178C Qualifiable Tool
Compiler/IDE
Requirements
Model
Source Code
Object Code
Simulink
Stateflow
SLRG: SDD *
Abbreviations
SL: Simulink
SLVNV: Simulink Verification and Validation
RMI: Requirements Management Interface
SDD: System Design Description
SLDV: Simulink Design Verifier
SLRG: Simulink Report Generator
PS: Polyspace
RTE: Run-Time Error
EC: Embedded Coder
PIL: Processor-in-the-Loop
Verify
Simulink Code
Inspector*
Trace
Conformance
Trace
Conformance
Verify
Verify
Verify
Verify
Verify
EC: PIL
SLRG
Polyspace*
Conformance
PS:MISRA-C
Checks *
Conformance
SLVNV: DO-178C/DO-331
Checks *
Verify
SLRG
SLVNV: Model Coverage *
Simulink Design Verifier
Verify
EC: PIL
SLRG
Polyspace*

## Slide 52: Questions?
Notes: [Timing: 15 minutes for Intro]